## Slide 1: CPU
NSWI170 Computer Systems
Jakub Yaghob, Martin Kruliš

## Slide 2: Semantic gap
Gap between user intent and instructions executed by CPU
c = http.connect();
req = c.postRequest();
req.setMultipart();
req.add(img, "image/png");
req.send();
I want to upload this meme to Discord…
compiler
LDW $r1, $r30
ADDI $r2, $r1, 1
SHL $r2, 2
STW $r30, $r2
JNE $r3, 0, $ip + 6
...
0110110110101010100101001001101010011010111010110101101101101010101001010010011010100110101110101101011...

## Slide 3: Von Neumann architecture
System architecture
  Program and data in the same memory
  One shared bus
    Evolution of the architecture
Notes: Picture taken from https://en.wikipedia.org/wiki/Von_Neumann_architecture
Program and data in the same memory – simplification of the hardware, complication for programmers (program can overwrite itself – used as a hack in the past, now avoided, some protection mechanisms exist)
How the data transfers on the shared bus works
Collisions
Input and output devices could look like memory from CPU (memory mapped devices)
IO devices can initiate direct memory transfers (DMA)

## Slide 4: Harvard architecture
Separate memory spaces
  With separate buses
  And separate addressing mechanism (instructions)
Still used in some SoC microcontrollers
Instruction Memory
Notes: Picture taken from https://en.wikipedia.org/wiki/Von_Neumann_architecture

## Slide 5: Real PC architecture
Sandy Bridge
mouse
LAN
Lan
Adap
South Bridge (PCH)
Audio Codec
DVD
Drive
Hard
Disk
Parallel Port
Serial Port
Floppy
Drive
PS/2 keybrd/ mouse
Cache
DDRIII
Channel 1
Mem BUS
DDRIII
Channel 2
Memory controller
Core
Core
D-sub, HDMI, DVI, Display port
External Graphics
Card
PCI express ×16
GFX
Display link
2133-1066 MHz
Line in
Line out
S/PDIF in
S/PDIF out
Super I/O
LPC
USB
SATA
SATA
BIOS
PCI express ×1
exp
slots
System Agent
4×DMI
Notes: Explain the blocks
Memory has the fastest buses and multiple channels, since it is the greatest bottleneck.
Many separate buses, each is peer-to-peer, avoids collisions (an analogy can be found in networking)
Hierarchical division, fast buses (controllers) integrated to the CPU die (mem bus, PCIe), others are deferred via south bridge.
Memory buses and internal CPU buses are massively parallel, external buses are mostly serial (PCIe has links, SATA, USB, LAN, …) – problems with sync. on multiple wires
GPU is the second important component, requires a lot of throughput (that is why it also has its own memory for caching the data)
Southbridge term is no longer used (explain Northbridge), now it is just generically called “chipset”.

## Slide 6: CPU
CPU Architecture
  Instruction Set Architecture (ISA)
    Abstract specification (contract between programmers and HW designers)
  Hardware architecture
    Actual implementation
What is CPU?
  "Simple" machine that executes instructions
    Instruction – simple command, arithmetic operation, …
  Registers, memory controllers, I/O
Notes: Examples for ISA (x86, IA64, MIPS, Risc-V) and and HW architectures (Intel Raptor Lake/Raptor Cove, AMD Zen 5)

## Slide 7: Instruction
Simple command to the CPU
  Binary encoding (CPU), assembler (programmers)
Operands
  Depending on ISA – max 1, 2, or 3 (some may be implicit)
  Register, immediate value
Fixed vs. variable lengths
Notes: The example is taken from https://en.wikipedia.org/wiki/Instruction_set_architecture

## Slide 8: Instruction cycle
Sub-steps performed in every instruction
  Load an instruction from the address stored in IP register
  Decode the instruction
  Load operands
  Execute the operation
  Store the result
  Increment IP
Some steps may be skipped for some instructions
Notes: IP = Instruction Pointer (also called Program Counter or PC)

## Slide 9: add execution example
reg. O
Simplified CPU using one internal bus
data bus
GR1_i
register R1
Adder unit O = A + B
reg. A
reg. B
GAA
GAB
GR1_o
…
Instruction decoder and scheduler
register R2
add r3 r1 r2 = GR1_out + GAA; GR2_out + GAB; ADD; GAO + GR3_in
GR2_i
GR2_o
GR3_i
register R3
GR3_o
GAO

## Slide 10: Instructions - motivation
How can we execute the following code?
  if (a < 3) b = 4; else c = a << 2;
  for (int i = 0; i < 5; ++i) a[i] = i;
  int f(int p) { return p + 1; }
  void g() { auto r = f(42); }
Notes: C++ is quite close to instructions.
Try to guess, how such instructions could look like (for the code snippets above).
Also mention relation to higher languages (like Python or even Haskell), scripting languages (bash, Python, PHP)

## Slide 11: Instruction classes
Load instructions
  Memory -> register
  Take a long time to execute, important to detect soon (fetch data ahead)
Store instructions
  Register/immediate -> memory
Move instruction
  Between registers
  x86-64 also between registers and memory
    Difficult to implement efficiently in HW

## Slide 12: Instruction classes
Arithmetic and logic instructions
  +, -, <<, >>, &, |, ^, ~
  *, /, %
Jumps
  Unconditional × conditional
  Direct × indirect × relative
Call, return
…
No funny stuff like "str" * 4
Tests required (==, <, …)

## Slide 13: Higher-level code structures
if (a < 3) b = 4; else c = a << 2;
  ...
  jge [a], 3
  store [b], 4
  jmp
  load r1, [a]
  shl r1, 2
  store [c], r1
  ...
This is just a symbolic abstract assembler (not an actual one)

## Slide 14: Higher-level code structures
for (int i = 0; i < 5; ++i) a[i] = i;
    mov r1, 0
    jge r1, 5
    load r2, [a]
    add r2, r2, r1
    store [r2], r1
    add r1, r1, 1
    jmp
    ...
Actually, the offset needs to be multiplied by sizeof(a[0]), but you got the point...

## Slide 15: Registers
Types
  General, integer, floating point,
  address, branch, flags, predicate,
  application, system,
  vector, …
Naming
  Direct (EAX, r01, …) × stack (relative addressing to top of the stack)
Aliasing
Notes: Address register – holds an address for a data operation
Branch register – holds an address for a jump instruction
Predicate registers – IA64 example with if-else (better than cond jump), instruction masking for vector instructions and SIMT execution (GPUs)
Stack naming – e,g,, 8087 ST(0), ST(1)…
Aliasing EAX, AX, AH AL

## Slide 16: Registers – example 32-bit x86
EAX | AX | AH | AL |  | CS |  |  | 
EBX | BX | BH | BL |  | DS |  |  | 
ECX | CX | CH | CL |  | ES |  |  | 
EDX | DX | DH | DL |  | SS |  |  | 
ESI |  | SI |  |  | FS |  |  | 
EDI |  | DI |  |  | GS |  |  | 
EBP |  | BP |  |  | EFLAGS |  | FLAGS | 
ESP |  | SP |  |  | EIP |  | IP | 
x86-64 extends registers to 64bits (RAX, RBX, …)
+ adds general regs. R8 - R15
Notes: Explain diff between 16bit, 32bit, and 64bit versions. Explain aliasing. Explain (non)orthogonal register sets.
A – Accumulator
B – Base
C – Counter
D – Data
SI – Source Index
DI – Destination Index
BP – Base Pointer
SP – Stack Pointer

## Slide 17: Registers – example IA-64
Notes: Note that some of the int and float registers have fixed value (0, 1).
FYI: IA-64 has currently no mainstream hardware implementations and was recently removed from Linux kernel…

## Slide 18: MIPS – simple assembler
Execution environment
  32-bit (almost general) registers r0-r31
    r0 is always 0, writes are ignored
    r31 is a link register for the jal instruction
  No stack (register)
    Realized by SW
  No flags
    Slightly different instruction set (especially tests and conditional jumps)
  Program Counter (PC) register
Notes: jal instructon is indirect jump (used for return from functions)

## Slide 19: Application Binary Interface
Application Binary Interface (ABI)
  Additional specification that accompanies ISA
  Prescribes how the CPU should be used
    Important for compiler designers
    If application and a library are compiled separately, they need to be compatible
  Binary interfaces between applications
    Typical utilization (meaning) of registers
    Stack implementation and layout
    Function call conventions
    …

## Slide 20: MIPS – register aliases
Register | Name | Purpose | Preserve
$r0 | $zero | 0 | N/A
$r1 | $at | Assembler temporary | No
$r2-$r3 | $v0-$v1 | Return value | No
$r4-$r7 | $a0-$a3 | Function arguments | No
$r8-$r15 | $t0-$t7 | Temporaries | No
$r16-$r23 | $s0-$s7 | Saved temporaries | Yes
$r24-$r25 | $t8-$t9 | Temporaries | No
$r26-$r27 | $k0-$k1 | Kernel registers – DO NOT USE | N/A
$r28 | $gp | Global pointer | Yes
$r29 | $sp | Stack pointer | Yes
$r30 | $fp | Frame pointer | Yes
$r31 | $ra | Return address | Yes
Notes: Preserve - a function must save/restore their values if these registers are used
Temporaries = ad-hoc intermediate values of expressions
Saved temporaries = temporaries with preserve flag
Kernel – syscall interface
Global pointer – reference to a frame were global variables are
Stack pointer – unlike x86, this is only ABI specification, there are no instructions that would rely on the fact that $r29 is the stack pointer
Frame pointer – additional pointer to stack that is used by functions (e.g., splits arguments and local variables), will be detailed later
Return address – saved by jal instruction (used for function calls)

## Slide 21: MIPS – instructions
Arithmetic
  add $rd,$rs,$rt
    R[rd] = R[rs] + R[rt]
  addi $rd,$rs,imm16
    R[rd] = R[rs] + signext(imm16)
  sub $rd,$rs,$rt
  subi $rd,$rs,imm16
Immediate value, 16 bit number encoded directly in the instruction itself
These are only symbolic placeholders, real example could look like add $r2,$r4,$r5
Signed extension to 32bits
(to match size of the registers)
Notes: Instruction add, addi, sub, and subi work on signed integers. For unsigned operations, there are counterparts with –u suffix (like addu).

## Slide 22: ISA comparison
MIPS
add $t1,$t1,$t0
addi $t1,$t1,1
add $t2,$t0,$t1
x86
add eax,ebx
add eax,1
or inc eax
mov eax,ebx
add eax,ecx

## Slide 23: MIPS – instructions
Logic operations
  and $rd,$rs,$rt andi $rd,$rs,imm16
  or $rd,$rs,$rt ori $rd,$rs,imm16
  xor $rd,$rs,$rt xori $rd,$rs,imm16
  nor $rd,$rs,$rt • R[rd] = R[rs] and/or/xor zeroext(imm16)
  No not instruction, use nor $rd,$rs,$rs
Shifts
  sll / slr $rd,$rs,shamt
    R[rd] = R[rs] << / >> shamt
  sra $rd,$rs,shamt
Arithmetic shift (keeps the sign)
Notes: Arithmetic shift can be used for signed integers (correctly fills in 0s or 1s from the left to preserve the sign of the int).
Note: There is no instruction for arithmetic left shift as shifting to left is the same for arithmetic and binary case.

## Slide 24: ISA comparison
MIPS
nor $t1,$t2,$t2
sll $t1,$t1,3
x86
mov eax,ebx
not eax
shl eax,3

## Slide 25: MIPS – instructions
Memory access
  lw $rd,imm16($rs)
    R[rd] = M[R[rs] + signext32(imm16)]
  sw $rt,imm16($rs)
    M[R[rs] + signext32(imm16)] = R[rt]
  lb $rd,imm16($rs)
    R[rd] = signext32(M[R[rs] + signext32(imm16)])
  lbu $rd,imm16($rs)
    R[rd] = zeroext32(M[R[rs] + signext32(imm16)])
  sb $rt,imm16($rs)
    M[R[rs] + signext32(imm16)] = R[rt]
Moves
  li $rd,imm32
    R[rd] = imm32
    Pseudo-instruction, translates to lui and ori
      Load upper immediate
  move $rd,$rs
    R[rd] = R[rs]
Notes: lw/sw – load/store 32bit word
lb/sb – load/store byte
lbu – unsigned load (simple zero extension instead of signed extension)

## Slide 26: ISA comparison
MIPS
lw $t1,1234($t0)
sw $t1,1234($t0)
lb $t1,1234($t0)
li $t1,5678
move $t1,$t0
x86
mov eax,[ebx+1234]
mov [ebx+1234],eax
mov al,[ebx+1234]
mov eax,5678
mov eax,ebx

## Slide 27: MIPS – instructions
Jumps
  j addr
    PC = addr
  jr $rs
    PC = R[rs]
  jal addr
    “Jump and link”
    R[31] = PC+4
    PC = addr
jal instruction (like all other instructions) takes 4 bytes in memory
Slightly different instruction format – the address is a 26bit immediate value

## Slide 28: ISA comparison
MIPS
j label
jr $ra
label:
jal fnc
x86
jmp label
jmp [ebx]
label:
call fnc
Placeholder that marks a place in the code, the actual address is computed by a compiler
This is double indirection!!! Register ebx holds address where is the pointer that is loaded and used as target address for the jump!
Return address stored to stack!
Notes: Note: jr $ra is single indirection (jumps to address stored in $ra).

## Slide 29: MIPS – instructions
Conditional jumps
  beq $rs,$rt,addr
    If R[rs] == R[rt] then PC = addr else PC = PC+4
  bne $rs,$rt,addr
    Analogical (not equal)
Testing
  slt / sltu $rd,$rs,$rt
    If R[rs]<R[rt] then R[rd] = 1 else R[rd] = 0
  slti / sltiu $rd,$rs,imm16
    If R[rs] < signext/zeroext(imm16) then R[rd] = 1 else R[rd] = 0
sltu is unsigned version of slt
Only lesser-than test, greater-than is created by swapping operands

## Slide 30: ISA comparison
MIPS
beq $t0,$t1,label
slt $t2,$t1,$t0
bne $t2,$zero,label
slti $t2,$t1,5
bne $t2,$zero,label
x86
cmp eax,ebx
jz label
cmp eax,ebx
jl label
cmp eax,5
jl label
Universal compare (result stored in flags)
Jump decision based on flags
Notes: cmp has similar semantics like subtraction
jz = jump if zero (flag is set)
jl = jump if lesser

## Slide 31: Code examples
Simple for-loop
for (int i = 0; i < N; i++) {
A[i] = 42;
}
addi $t0, $gp, 28 # $t0 <- address of A
lw $t1, 4($gp) # fetch N
move $t2, $zero # i = 0
ori $t3, $zero, 42 # $t3 = 42
j cond # go to condition
body:
sll $t4, $t2, 2 # i*4 -> offset
add $t4, $t4, $t0 # A+i*4
sw $t3, 0($t4) # A[i] = 42
addi $t2, $t2, 1 # i = i+1
cond:
slt $t4, $t2, $t1 # are we there yet?
bne $t4, $zero, body # no, we're NOT done
Notes: Based on https://courses.cs.washington.edu/courses/cse378/03wi/lectures/mips-asm-examples.html

## Slide 32: Code examples
i = N*5+3;
lw $t0, 4($gp) # fetch N
sll $t1, t0, 2 # N*4
add $t1, $t1, t0 # N*4+N
addi $t1, $t1, 3 # N+3
sw $t1, 0($gp) # i = ...
lw $t0, 4($gp) # fetch N
ori $t1, $zero, 5 # 5
mult $t0, $t0, $t1 # N*5 (fake)
addi $t0, $t0, 3 # N*5 + 3
sw $t0, 0($gp) # i = ...
Code can be optimized…
Multiplication is more complex as the result needs to be stored in 2 registers (but we have simplified it here)
Notes: Based on https://courses.cs.washington.edu/courses/cse378/03wi/lectures/mips-asm-examples.html

## Slide 33: Flags
Only used by some ISA
Control execution
Check status of the last instruction
Usual flags
  Z – zero flag
  S – sign flag
  C – carry flag
  O – overflow flag
x86 example
Notes: Very complex semantics which instructions affect which flags. For example,
add – sets all arithmetic flags
inc – sets almost all (ignores CF)
and – sets CF = 0 (always)
mov – does not affect anything

## Slide 34: ISA consolidation
Instruction set architecture
  Abstract model of CPU
Classification
  CISC – Complex Instruction Set Computer
  RISC – Reduced Instruction Set Computer
  VLIW – Very Long Instruction Word
  EPIC – Explicitly Parallel Instruction Computer
Orthogonality
  Accumulator
Load-Execute-Store
Notes: CISC – example x86
RISC – example ARM
Was true in the past, no longer true (x86 uses RISC-like core for microinstructions, ARM or MIPS have been extending their instructions sets steadily, so it is hard calling it “reduced” nowadays)
VLIW – multiple instructions encoded together to easily exploit instruction-level parallelism (they are executed concurrently) – e.g., Intel i860, IA64 (itanium), AMD GPUs (TeraScale, up to 2010, abandoned with GCN arch.)
EPIC – moving beyond VLIV
Explicitly declare dependencies between bundles of instructions (allowing grouping the bundles – e.g., in future hw generations)
More opportunities for speculative loads and instruction execution
Multiway branch instructions, emphasis on predicated execution (predicate registers instead of branching)
Example: Itanium

## Slide 35: Hardware architecture
CPU comprise…
  Memory controller
  Cache hierarchy
  Core
    Registers
      Types
    Logical processor
      Hyper threading
Note that HW registers and ISA registers do not need to match exactly (e.g., x86 register remapping)

## Slide 36: CPU – simplified scheme
CORE 0
T0
T4
EU
L1I
L1D
L2
CORE 1
T1
T5
EU
L1I
L1D
L2
CORE 2
T2
T6
EU
L1I
L1D
L2
CORE 3
T3
T7
EU
L1I
L1D
L2
L3/LLC
Package
Notes: Cache latencies
https://www.7-cpu.com/cpu/Skylake.html
https://gist.github.com/jboner/2841832

## Slide 37: Scheme of Real CPU (Package)
Intel Coffee Lake

## Slide 38: Real CPU
Scheme of one core

## Slide 39: Real CPU Die

## Slide 40: CPU architecture – pipeline
Current CPU
  14-19 stages

## Slide 41: CPU architecture – superscalar processor
Current CPU
  5-way, asymmetric
Notes: Contemporary CPUs are superscalar, but also asymmetric (e.g., Intel example – there were 4 simple decoders and one full decoder).

## Slide 42: CPU architecture – out-of-order execution
Decoder
Reservation station (pool)
µOPs
I/V ALU
Port 0
Port 1
Port 5
Port 6
Port 2
Port 3
Port 4
Port 7
I/V ALU
AGU
AGU
AGU
I ALU
I/V ALU
AGU
Load
Load
I Logic
Branch
I/F DIV
SQRT
AES
F FMA
String
I/V Logic
I/V MUL
F FMA
Bit scan
I/V Logic
I/V MUL
Comp Int
F ADD
Vec Shuff
Store
Branch
Reorder buffer
Notes: ALU = Arithmetic Logic Unit
AGU = Address Generation Unit
FMA = Fused Multiple-Add (a = b*c + d)
…

## Slide 43: Discussion
Notes: If you wish to learn more about low-level CPU principles, a good place to start could be https://simulator.io/samples#sample10